## Slide 1: Pi Camera - Spy Camera

## Slide 2: Getting set up
Connect a USB cable to the power
Login with username pi and password raspberry
Load the LX Terminal
At the command prompt enter sudo raspi-config
At the menu, navigate to Enable Camera
Select Enable
Select Finish
Select Yes to reboot

## Slide 3: Testing the camera
At the command prompt enter
raspistill -o image.jpg
On the screen you should see a preview appear for a few seconds, and then change briefly while the image is captured

## Slide 4: Using Python to Spy
import time
import picamera
with picamera.PiCamera() as camera:
camera.start_preview()
time.sleep(5)
camera.capture('/home/pi/Desktop/image.jpg')
camera.stop_preview()

## Slide 5: Other camera settings
camera.sharpness = 0 camera.contrast = 0 camera.brightness = 50 camera.saturation = 0 camera.ISO = 0 camera.video_stabilization = False camera.exposure_compensation = 0 camera.exposure_mode = 'auto' camera.meter_mode = 'average' camera.awb_mode = 'auto' camera.image_effect = 'none' camera.color_effects = None camera.rotation = 0 camera.hflip = False camera.vflip = False camera.crop = (0.0, 0.0, 1.0, 1.0)

## Slide 6: Video Capture
import time
import picamera
with picamera.PiCamera() as camera:
camera.start_preview()
camera.start_recording('/home/pi/Desktop/video.h264')
time.sleep(5)
camera.stop_recording()
camera.stop_preview()

## Slide 7: Sl--ow --- Mo
import time
import picamera
VIDEO_DAYS = 5
FRAMES_PER_HOUR = 1
FRAMES = FRAMES_PER_HOUR * 24 * VIDEO_DAYS
def capture_frame(frame):
with picamera.PiCamera() as cam:
time.sleep(2)
cam.capture('/home/pi/Desktop/frame%03d.jpg' % frame)
# Capture the images
for frame in range(FRAMES):
# Note the time before the capture
start = time.time()
capture_frame(frame)
time.sleep(
int(60 * 60 / FRAMES_PER_HOUR) - (time.time() - start)

## Slide 8: Enter the line into the LX terminal to render the video. ALL ON ONE LINE
ffmpeg -y -f image2 -i
-i /home/pi/Desktop/frame%03d.jpg
-r 24 -vcodec libx264 -profile
-profile high -preset
-preset slow /ho /home/pi/Desktop/timelapse.mp4